## Slide 1: The HelpichaIr
Dawson Green
Tony Muilenburg
Luis Santiago

## Slide 2: Previous Work
Rhino Arm Wheelchair
  The Helpichair was initially based upon a design that used a Rhino Robotics XR-3 Rhino Robotic Arm to assist a wheelchair bound individual with manipulating the environment around them.
  Previous Design has many well Documented Problems

## Slide 3: Hardware Implementation
4 Degrees of Freedom of Motion
Spoon Position Set by Cartesian Arm
  Built mostly from reused parts
OpenCV powered Position Analysis
  Provides data for tracking where spoon is during eating process
  1 camera (horizontal-vertical axes) implemented at this time

## Slide 4: Kinematics
Arm Weight: 5 pounds or 2.26Kg
X-axis Torque: 0.436 Nm
Y-axis Torque: 0.288 Nm
Z-axiz Torque: 0.071 Nm
Values
rx=19mm
ry=13mm
rz=3.18mm
Mass = 2.26kg
G= 9.81

## Slide 5: Software Design
Vision
Open CV
Code
Motor Control Code
Motor for Z axis
Stepper Motor Controller
Arduino
Servo X axis
Servo Y axis
Servo for spoon control

## Slide 6: OpenCV Vision
  Capture image from camera
  Use HSV, erode, dilate filters and then some centroid functions.
  After image filtered subtract distance on pixels
  Pass the results to control program convert into instructions to the motors

## Slide 7: Software
User interface framework coded in Visual Studio C++
Reads position data from output of OpenCV program
Establishes connection with motors
Performs basic diagnostics, permits manual control and maintains algorithm for patient feeding process
OpenCV position data is translated into motor rotational speeds via fuzzy logic algorithm

## Slide 8: Firmware (Arduino)
Interface features
  Reads commands via serial port access
  Controls multiple axes simultaneously
  Permits repeatable spoon motion
  Allows user to set servo continuous speed
Sample Firmware Code
// check serial buffer has something
if (Serial.available() > 0) {
// read first byte on serial and store it
int inByte = Serial.read();
// check if it is one the defined cases
switch (inByte) {
case 'x':
// Valid case, wait for an int and store it in pos
pos = Serial.parseInt();
// provides feedback for debuf if needed
#ifndef Silent
Serial.print("Servo X=");
Serial.println(pos);
#endif /* Silent */
xservo.write(pos);
break;

## Slide 9: Firmware (Stepper Motor)
Interface features
  Reads commands via serial port access
  Ramps motor speed to reduce stress on system components
  Provides high precision motor control
  Motor can lock into position and support significant stress

## Slide 10: Challenges
Weight and cost
Vision filters are very sensitive to room lighting
Arm Construction Very Time Consuming
Controlling Servo Speeds

## Slide 11: Demo

## Slide 12: Future Work
Automate Helpichair motion using vision
Built a Stronger arm
Make arm rotate
Electric Circuit to operate permanently of batteries
Utilize a genetic algorithm to optimize Helpiarm motions

## Slide 13: Resources
Code, videos, Data Sheets and Development Documents available at
http://smartwheelchair.themuilenburgs.com
Visual Studio can be obtained from Dreamspark website via CAT: click here
(if link is broken just go to CAT website and type Microsoft in search)
Arduino IDE and instructions can be found at Arduino website
http://arduino.cc/en/Main/Software

## Slide 14: Questions